SECTION 08 30 00

SPECIALTY DOORS

Part 1	GENERAL

1.1	Summary

A.	Section Includes: Glass doors with extruded aluminum rails with decorative metal cladding

B.	Related Sections:

1. 08 06 10 – Door schedule.

2. 08 06 71 – Door hardware schedule.

3. 08 13 19 – Stainless steel doors.

4. 08 71 00 – Door hardware.

5. 08 80 00 – Glazing.

1.2	References

A.	ASTM International

1. ASTM C 1036 Specification for Flat Glass

2. ASTM C 1048 Specification for Heat-Treated Flat Glass-Kind HS, Kind FT Coated and Uncoated Glass

3. ASTM C 1172 Specification for Laminated Architectural Flat Glass

4. ASTM E-774-Specification for Sealed Insulating Glass Units where insulating glass is specified

B.	ANSl - American National Standards Institute

1. ANSI Z-97.1 Safety Performance Specifications and Methods of Test Used in Buildings

2. CPSC 16 CFR 1201 Safety Standard for Architectural Glazing Materials, Category I and II

1.3	Submittals

A.	Provide submittals in accordance with Section 01 33 00 – Submittal Procedures.

B.	Submit manufacturer’s shop drawings, installation drawings, installation instructions and maintenance instructions.

C.	Submit environmental impact data for all materials.

D.	Submit samples no less than 4" x 4" for all specified material finishes.

E.	Manufacturer information:

1.	Provide overview literature describing manufacturer’s overall scope of products and manufacturing capabilities.

2.	Provide URL for manufacturer’s website; website must provide access to technical data, images and general product information.

1.4	Quality Assurance

A.	Manufacturer Qualifications

1.	Minimum 10 years experience in the manufacture of architectural surface materials.

2.	Minimum 10 years experience in the fabrication of doors.

3.	Provide reference list of at least 10 public space projects currently using doors fabricated by the manufacturer.

B.	Installer Qualifications

1.	Minimum three years experience in the installation of doors.

1.5	Delivery, Storage and Handling

A.	Deliver materials to installation site in manufacturer’s original packaging. Handle products in accordance with manufacturer’s instructions. Store in dry, secure location, protected against direct sunlight and excessive heat. Protect finished surfaces with strippable film.

1.6	Warranty

A.	Provide manufacturer’s standard warranty.

1.	Warranty terms: one year against defects in materials and workmanship.

Part 2	PRODUCT

2.1	Manufacturer

A.	Forms+Surfaces

30 Pine Street

Pittsburgh, PA 15223

phone: 800-451-0410

fax: 412-385-4715

email: sales@forms-surfaces.com

website: www.forms-surfaces.com

2.2	Door Type

A.	General

1.	Provide laminated glass doors with decorative metal rails

B.	Glass

1.	Glass Doors

a.	Material: VividGlass: ViviChrome Chromis, ViviChrome Metallic, ViviChrome Scribe, ViviGraphix Graphica, VivGraphix Gradiance, ViviSpectra Elements, ViviSpectra Spectrum, ViviSpectra VEKTR, ViviSpectra Zoom, ViviStone Abalone Onyx, ViviStone Cream Onyx, ViviStone Honey Onyx, ViviStone Opal Onyx, ViviStone Pearl Onyx, ViviStone White Onyx, ViviStrata Monolithic, ViviStrata Layers, ViviTela Loom, ViviTela Mesh, ViviTela Shibori (choose one)

b.	Material: CastGlass: Classic Monolithic Atlantis, Classic Monolithic Hikaru, Classic Monolithic Nuv’eau, Classic Monolithic On-Wa, Classic Monolithic Pietra, Classic Monolithic Plank, Classic Monolithic Rake, Classic Monolithic Spruzzo, Classic Monolithic Tanami, Classic Monolithic Valencia, Intervals Monolithic Coda, Intervals Monolithic Locus, Intervals Monolithic Octave, Intervals Monolithic Origin, Intervals Monolithic Prose, Intervals Monolithic Verse, Profile Monolithic Chase 12, Profile Monolithic Chase 25, Profile Monolithic Corduroy (choose one)

2.2	Rails

A.	Rail Configuration

1.	Rails are extruded aluminum with decorative metal cladding.

2.	Rail Shape: Square Rail, Beveled Rail (choose one)

B.	Rail Cladding Metal

1.	Stainless Steel Rails

a.	Finish: Mirror, Satin (choose one)

2.	Bronze Rails

a.	Finish: Oil-Rubbed

3.	Brass Rails

a.	Finish: Polished

2.3	Hardware Preparation and Supplied Hardware

A.	Hardware “Prep Only”

1.	Per Contract Documents and approved drawings, provide doors with “prep only” for required hardware as specified. Hardware to be supplied by others.

B.	Hardware “Prep-and-Supply”

1.	Per Contract Documents and approved drawings, provide doors with “prep-and-supply” hardware package as specified.

Part 3	EXECUTION

  - Examination

A.	Verify that dimensions are correct and project conditions are suitable for installation. Do not proceed with installation until unsatisfactory conditions have been corrected.

3.2	Installation

A.	Install doors in accordance with manufacturer’s instructions, referenced standards and approved drawings.

B.	Ensure that doors are installed plumb and true, free of warp or twist, within tolerances specified in referenced standards and approved drawings.

  - Adjust and Clean

A.	Test and verify correct operation of doors and related hardware. Adjust as needed.

B.	Clean doors in accordance with manufacturer’s instructions.

END OF SECTION