DIVISION 26 00 00					ELECTRICAL

SECTION 26 50 00 				LIGHTING

SECTION 26 56 00 				EXTERIOR LIGHTING

LIGHTHOUSE BOLLARD

Part 1		General

- Summary

  - Section Includes:

    - Compact fluorescent bollard.

    - High intensity discharge bollard.

- Submittals

  - Provide submittals in accordance with Section 01 33 00 – Submittal Procedures.

  - Product data:

    - Manufacturer’s standard product literature.

    - Shop drawings.

    - Installation instructions.

    - Maintenance instructions.

  - Submit powdercoat finish samples for approval.

- Quality Assurance

  - Manufacturer Qualifications:

    - Minimum 15 years experience in the manufacture of outdoor lighting.

    - Provide reference list of at least ten major transportation authorities, municipalities, universities, or

other high-use public environments currently using outdoor lighting fabricated by the manufacturer.

- Delivery, Storage and Handling

  - Handle products in accordance with manufacturer’s instructions.

  - Store products in manufacturer’s original packaging until ready for installation.

  - Protect products from impacts and abrasion during storage.

- Warranty

  - Provide manufacturer’s standard warranty.

    - Warranty terms: three years from date of invoice against defects in materials and workmanship.

Part 2		Products

- Manufacturer

  - Basis-of-design product: provide bollards based on the product named:

    - Lighthouse Bollard by Forms+Surfaces

    - Manufacturer Contact:
Forms+Surfaces
30 Pine Street
Pittsburgh, PA 15223
phone: 800-451-0410

fax: 412-385-4715

email: sales@forms-surfaces.com

website: www.forms-surfaces.com

  - Bollards

    - Materials

      - Column: tapered one-piece cast aluminum with horizontal score lines.

      - Head: three-part cast aluminum with frosted borosilicate glass cylinder, gasketed top and bottom.

      - Ballast (Select one below depending on model):

        - High intensity discharge bollard.

            - F-can ballast, thermally protected, 120/277V, -27°F starting temperature, class B sound rating.

        - Compact fluorescent bollard.

            - Electronic, thermally protected, 120/277V combination for 26W, 32W or 42W compact fluorescent lamp, less than 10% THD, 0°F starting temperature.

      - Lamp (Select one lamp below):

        - Compact fluorescent bollard.

            - CFM26:

              - 26W triple tube 4-pin.

              - Base: GX24q-3.

              - Luminaire lumens: 424.

              - Color temperature: 4,100K.

            - CFM42:

              - 42W triple tube 4-pin.

              - Base: GX24-q4.

              - Luminaire lumens: 779.

              - Color temperature: 4,000K.

        - High intensity discharge bollard.

            - M70:

              - 70W metal halide.

              - Base: medium.

              - Luminaire lumens: 1,364.

              - Color temperature: 4,000K.

    - Finishes: polyester powdercoat (Select one option below):

      - Standard Texture from Forms+Surfaces Powdercoat Chart.

      - Premium Texture from Forms+Surfaces Powdercoat Chart.

      - Custom RAL powdercoat color.

    - Dimensions

      - Overall: 10.6" diameter x 41.9" high.

    - Mounting: Surface Mount with J-bolts. 0.25" thick stainless steel base plate included. Stainless steel mounting hardware sold separately. Template available upon request.

Part 3		Execution

- Examination

  - Verify that substrates are stable and capable of supporting the weight of items covered under this section.

  - Verify that substrates have been adequately prepared to securely anchor those items that will be surface

mounted.

- Installation

  - Install according to the manufacturer’s installation instructions.

  - Install in conformance to applicable ADA guidelines and End User’s established Accessibility policies.

END OF SECTION