DIVISION 12 00 00					FURNISHINGS

SECTION 12 93 00 				SITE FURNISHINGS

SECTION 12 93 43 				SITE SEATING AND TABLES

SECTION 12 93 43.13 		SITE SEATING

TRANSIT SEATING

Part 1		General

- Summary

  - Section Includes:

    - Single-sided backless bench, angled seat.

    - Single-sided backless bench, angled seat.

    - Single-sided backless bench, horizontal seat.

    - Single-sided backed bench, angled seat.

    - Single-sided backed bench, horizontal seat.

    - Double-sided backless bench, angled seat.

    - Double-sided backless bench, horizontal seat.

    - Double-sided backed bench, angled seat.

    - Double-sided backed bench, horizontal seat.

- Submittals

  - Provide submittals in accordance with Section 01 33 00 – Submittal Procedures.

  - Product data:

    - Manufacturer’s standard product literature.

    - Shop drawings.

    - Installation instructions.

    - Maintenance instructions.

- Quality Assurance

  - Manufacturer Qualifications:

    - Minimum 15 years experience in the manufacture of site seating.

    - Provide reference list of at least ten major transportation authorities, municipalities, universities, or

other high-use public environments currently using site seating fabricated by the manufacturer.

- Delivery, Storage and Handling

  - Handle products in accordance with manufacturer’s instructions.

  - Store products in manufacturer’s original packaging until ready for installation.

  - Protect products from impacts and abrasion during storage.

- Warranty

  - Provide manufacturer’s standard warranty:

    - Warranty terms: three years from date of invoice against defects in materials and workmanship.

Part 2		Products

- Manufacturer

  - Basis-of-design product: provide backed and/or backless benches/perches based on the product named:

    - Transit Seating by Forms+Surfaces.

    - Manufacturer Contact:
Forms+Surfaces
30 Pine Street
Pittsburgh, PA 15223
phone: 800-451-0410

fax: 412-385-4715

email: sales@forms-surfaces.com

website: www.forms-surfaces.com

  - Seating

    - Materials:

      - Bench legs: 3" diameter tubular stainless steel.

      - End castings: cast stainless steel.

      - Seats and backrests: stainless steel sheet with 1/2" diameter perforations.

      - Armrests: formed from 1.5" stainless steel bar.

    - Finishes:

      - Bench legs: radial Satin finish.

      - End castings: bead-blasted finish.

      - Seats and backrests:

        - Satin finish.

        - Polyester powdercoat (Select one option below):

            - Standard Texture/ Gloss from Forms+Surfaces Powdercoat Chart.

            - Custom RAL powdercoat color.

      - Armrests: Satin finish.

    - Dimensions (Select model(s) below):

      - Single-sided backless bench, angled seat:

        - Overall: 74.4" long x 16.5" deep x 22.3" high.

        - Seat: 72" long x 13" deep x 18" high*.

      - Single-sided backless bench, horizontal seat:

        - Overall: 74.4" long x 16.5" deep x 22.7" high.

        - Seat: 72" long x 13" deep x 18" high.

      - Single-sided backed bench, angled seat:

        - Overall: 74.4" long x 16.5" deep x 31.4" high.

        - Seat: 72" long x 13" deep x 18" high*.

      - Single-sided backed bench, horizontal seat:

        - Overall: 74.4" long x 16.5" deep x 31.4" high.

        - Seat: 72" long x 13" deep x 18" high.

      - Double-sided backless bench, angled seat:

        - Overall: 74.4" long x 30" deep x 22.3" high.

        - Seat: 72" long x 13" deep x 18" high*.

      - Double-sided backless bench, horizontal seat:

        - Overall: 74.4" long x 30" deep x 22.7" high.

        - Seat: 72" long x 13" deep x 18" high.

      - Double-sided backed bench, angled seat:

        - Overall: 74.4" long x 30" deep x 31.4" high.

        - Seat: 72" long x 13" deep x 18" high*.

      - Double-sided backed bench, horizontal seat.

        - Overall: 74.4" long x 30" deep x 31.4" high.

        - Seat: 72" long x 13" deep x 18" high.

*Seat heights as measured as front edge of seat. Horizontal seats are flat; angled seats slope upward to a height of 19.8" at the

back of the seat.

    - Mounting: (Select one option below):

        - Cast in place

        - Surface mount: Stainless steel anchors and mounting bolts are sold separately.

Part 3		Execution

- Examination

  - Verify that substrates are stable and capable of supporting the weight of items covered under this section.

  - Verify that substrates have been adequately prepared to securely anchor those items that will be surface

mounted.

- Installation

  - Install according to the manufacturer’s installation instructions.

  - Install in conformance to applicable ADA guidelines and End User’s established Accessibility policies.

END OF SECTION